## Slide 1: CSE 4128 Image Processing and Computer Vision Laboratory Week 2: Segmentation(Edge Detection)
Dr. Sk. Md. Masudul Ahsan
Professor
Dept. of CSE, KUET
Dipannita Biswas
Lecturer
Dept. of CSE, KUET

## Slide 2: Segmentation
Segmentation subdivides an image into its constituent regions or objects.
Separating objects from the background and giving them individual labels(ID numbers)
Segmentation attempts to partition the pixels of an image into groups that strongly correlate with the objects in an image

## Slide 3: Edge Detection
It is most frequently used for segmenting images based on abrupt(local) changes in intensity. It centers around contour detection.
An edge is a set of connected pixels that lie on the boundary between two regions
Edge models

## Slide 4: Edge and Derivatives
Derivatives are used
to find discontinuities.
1st derivative tells us
where an edge is.
2nd derivative can be used to show edge side

## Slide 5: Segmentation with Edge Detection
Input
Convolving with LoG kernel with Sigma = 1, kernel size= 7X7
Applying Zero-crossing
Applying thresholding
(local sigma >60)

## Slide 6: Robust Laplacian-based Edge Detector
LoG
operator
image
zero
crossing?
estimate
local variance
2>th
2
not an
edge point
No
yes
No
not an
edge point
edge
point

## Slide 7: Laplacian Of Gaussian
The Laplacian of Gaussian (or Mexican hat) filter uses the Gaussian for noise removal and the Laplacian for edge detection
this can also be performed by smoothing with a Gaussian kernel and then taking its Laplace, we can obtain the Laplacian of the Gaussian kernel.
Laplacian:
Gaussian:

## Slide 8: Zero crossing and Thresholding
1 | 1 | 1 | -1 | 1
3 | 3 | -3 | 3 | 4
3 | 4 | 4 | 3 | 1
1 | -1 | 1 | 1 | 2
1 | 2 | -2 | 1 | 2
0 | 0 | 0 | 0 | 0
0 | 3 | -3 | 3 | 0
0 | 4 | 4 | 0 | 0
0 | -1 | 1 | 0 | 0
0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0
0 | 255 | 255 | 255 | 0
0 | 0 | 255 | 0 | 0
0 | 0 | 255 | 0 | 0
0 | 0 | 0 | 0 | 0
zero
crossing
2>
threshold
= 2.5 ,
Threshold = 2

## Slide 9: Laplacian Edge Detection
f
f’
f’’
zero crossing
Laplacian
operator
image
zero-crossing
edge
map
f(x,y)
g(x,y)
E(x,y)
Unlike first-order filters that detect the edges based on local maxima or minima, Laplacian detects the edges at zero crossings i.e. where the value changes from negative to positive and vice-versa.

## Slide 10: Assignment
Create a region-based segmentation method applying the splitting technique.
Instructions:
Use RGB image.
Show the change in the merged image with the variation of the threshold, which will be user-input.

## Slide 11: Algorithm
It starts with the assumption that the entire image is homogeneous.
Homogeneity can be considered as the standard deviation of the sub-image < threshold.
Check if the image is homogenous:
    If this is not true, the image is split into four sub-images.
    This splitting procedure is repeated recursively until we split the image into homogeneous regions.
Return the concatenated split sub-images.

## Slide 12: Quadtree
If the original image is square N x N, all regions produced but the splitting algorithm are squares having dimensions M x M.
Since the procedure is recursive, it produces an image representation that can be described by a tree whose nodes have four sons each. Such a tree is called a Quadtree.
R0
R1
R2
R3
R0
R1
R00
R01
R02
R04
R2
R3

## Slide 13: Output Results
Input image
Split into 2X2 and merge
Output image, with threshold 25